## Slide 1
Real-time locating system (RTLS) using Ultra-Wide Band
Ms. Beerelly Srinitha,
CS20B1004,
IIIT Raichur

## Slide 2
Problem Statement
Introduction
Related Works
Ultrawide Band
  Localization Techniques and Positioning Algorithms
Methodology
Proposed Architecture
Proposed Algorithm
Simulation
  Localization Simulation
  LOS and NLOS Scenarios
  Importance of Number of Anchors
  Trajectory Prediction Using LSTM Model
  Optimal Anchors Position Recommendation System
Conclusion
Contents

## Slide 3
In an era where accuracy, precision and efficiency reign supreme, businesses and industries are constantly seeking innovative solutions to streamline their operations.
One such groundbreaking technology making waves in various sectors is RTLS. It is a sophisticated framework designed to accurately track and monitor the real-time location of assets, personnel, or any desired object within a defined space.
Problem Statement

## Slide 4
Ultrawide Band
Bandwidth | 500 MHz
Data rate | 7 to 27 megabits per second
Frequency range | 3.1 and 10.6 GHz
Battery | Low consumption
Range | up to 200 meters (656 feet) based on the IEEE 802.15.4a standard(200 for ESP32 UWB PRO)
Accuracy | 10 cm (3.9 inches)
Cost | 2000 – 5000 INR
Best For | Proximity Marketing, Customer Analytics, Indoor Navigation, Smart Homes, Factory Automation, Asset-Tracking, Logistics
Fig 1. DW1000 UWB Module
Fig 2. DW3000 UWB Module
Introduction

## Slide 5
Related Works

## Slide 6
Localization Techniques and Position Calculation Algorithms
Interpretation of Data
  TOF - Using Two-way time-of-arrival(TW-TOA)
  Time-difference-of-arrival (TDOA)
Position Calculation Algorithms
  Trilateration
  Triangulation

## Slide 7
Time of Flight(TOF) -
Using Two Way Time Of Arrival(TW-TOA)
TOF is a method based on two way ranging.
Tag needs to send and receive signals of the anchor several times
Fig 3. TOF For Localization

## Slide 8
Time Difference Of Arrival (TDOA)
The UWB tag will send out poll message and all the nearby UWB anchors will receive it and record the arrival time
Fig 4. TDOA For Localization

## Slide 9
Position Calculation Algorithms
Trilateration
Fig 5. Trilateration
Triangulation
Fig 6. Triangulation

## Slide 10
Methodology

## Slide 11
Proposed Architecture

## Slide 12
Proposed Algorithm

## Slide 13
Simulation
The following is the simulation scenario of UWB localization using Matlab
TDOA is used in this simulation for localization.
Parameters | Values
Tag Initial Location | [50 50]
Anchor 1 Location | [40 41]
Anchor 2 Location | [62 83]
Anchor 3 Location | [87 24]
Tag Velocity | [0.5, 0.2]
Simulation Area | 100 x 100
Fig 7. Simulation Scenario (3 anchors and 1 tag).
Table 1. Simulation Parameters

## Slide 14
Case 1: Anchors and Tags are Fixed
Fig 8. Localization of the tag in static case using UWB
Fig 9. Zoomed in Version of Fig 11

## Slide 15
Case 2: Anchors are Fixed and Tag is Dynamic
Fig 10. Localization of the tag in dynamic case using UWB
Fig 11. Simulation of localization in dynamic case

## Slide 16
LOS and NLOS Scenario
Case 1: Line Of Sight
Case 2: Non Line Of Sight

## Slide 17
Importance of Number of Anchors
Case 1: One Anchor (LOS)
Case 2: Two Anchors (LOS)

## Slide 18
Floor Map Features:
Fig 13. Floor Map
Parameters | Values
Size | 400 * 600 Sq.Ft
Map Type | 1BHK
Table 2. Floor Map Characteristics
Optimal Anchor Position Recommendation System

## Slide 19
Cases:
Fixed:
  Number of Tags : Fixed
  Number of Anchors : Fixed
  Tags positions : Randomly generated
  Anchor positions : Predicted.
Parameters | Values
Number of Tags | 5
Number of Anchors | 3
Table 3. Simulation Parameters
Randomly Generated Tag Positions

## Slide 20
Fig 14 . Floor Map with Tags and Anchors Positioned
Predicted Anchor Positions
Anchor
Tag

## Slide 21
Cases:
2. On Demand:
  Number of Tags : By the user
  Number of anchors : By the user
  Tags positions : Randomly generated
  Anchor positions : Predicted.
Parameters | Values
Number of Tags | By user
Number of Anchors | By user
Table 4. Simulation Parameters
Input taken from User and Tag positions are Randomly generated

## Slide 22
Fig 15 . Floor Map with Tags and Anchors Positioned
Predicted Anchor Positions
Anchor
Tag

## Slide 23
Cases:
3. No Demand:
  Number of Tags : By the user
  Number of anchors : Automatically assigned by the algorithm
  Tags positions : Randomly generated
  Anchor positions : Predicted.
Table 5. Simulation Parameters
Parameters | Values
Number of Tags | By user
Number of Anchors | By Algorithm
Input taken from User and Tag positions are Randomly generated

## Slide 24
Fig 15 . Floor Map with Tags and Anchors Positioned
Predicted Anchor Positions
Anchor
Tag

## Slide 25
num_time_steps = 99
num_time_steps = 59
Trajectory Prediction Using LSTM Model

## Slide 26
Real time Scenario
Detecting
Locating
Tracking and Predicting
UWB Supporting Models

## Slide 27
Conclusions
UWB localization was virtually executed. Simulations for different scenarios were performed
Developed an LSTM model to predict the path trajectory of the tag.
Environments like LOS and NLOS were evaluated.
Importance of the number of anchors was discussed .
Optimal anchor recommendation system was proposed.

## Slide 28
References
[1] Al-Ammar MA, Alhadhrami S, Al-Salman A, Alarifi A, Al-Khalifa HS, Alnafessah A, Alsaleh M. Comparative survey of indoor positioning technologies, techniques, and algorithms. In2014 International Conference on Cyberworlds 2014 Oct 6 (pp. 245-252). IEEE.
[2] Djaja-Josko V, Kolakowski J. A new method for wireless synchronization and TDOA error reduction in UWB positioning system. In2016 21st International Conference on Microwave, Radar and Wireless Communications (MIKON) 2016 May 9 (pp. 1-4). IEEE.
[3] Zandian R, Witkowski U. Implementation challenges of synchronisation of UWB nodes in TDoA structures. In2018 International Conference on Indoor Positioning and Indoor Navigation (IPIN) 2018 Sep 24 (pp. 1-8). IEEE. 4] Tiemann J, Eckermann F, Wietfeld C. Atlas-an open-source tdoa-based ultra-wideband localization system. In2016 International Conference on Indoor Positioning and Indoor Navigation (IPIN) 2016 Oct 4 (pp. 1-6). IEEE. 5] Chen J, Shi T, Liu Y, Wu S. A time-compensation TDOA-based wireless positioning method for multi-level IoT positioning. In2019 15th International Wireless Communications & Mobile Computing Conference (IWCMC) 2019 Jun 24 (pp. 1731-1736). IEEE.
[6] Sidorenko J, Schatz V, Scherer-Negenborn N, Arens M, Hugentobler U. Error corrections for ultrawideband ranging. IEEE Transactions on Instrumentation and Measurement. 2020 May 22;69(11):9037-47.
[7] Sathyan T, Sinha A, Kirubarajan T. Passive geolocation and tracking of an unknown number of emitters. IEEE Transactions on Aerospace and Electronic Systems. 2006 Apr;42(2):740-50.

## Slide 29
Thank You